## Slide 1
Precision Pen-Plotter for Mechatronics
Team Members: Aman Patel, Vighnesh Deshmukh, Deep Shah, Rishabh Deshkar, Atharva Bhosale
University: Hochschule Schmalkalden – University of Applied Sciences
Date: July 24, 2025

## Slide 2
Project Introduction & Motivation
1
Mechatronics Workshop Project
Selected as our Master's program centerpiece, applying theoretical knowledge to a tangible system.
2
Inspired by "Nikola's House"
Aim to recreate a complex drawing using a fully custom-built motion platform.
3
Hands-On Application
Practical application of control systems, mechanical design, and embedded hardware development.

## Slide 3
Use Case & Core Objectives
Primary Goal: Draw Nikola's House
The system must accurately plot the intricate design three times in succession, demonstrating high reliability and consistency.
Key Performance Indicators
Precision & Repeatability: Consistent output across multiple iterations.
Emergency Stop: Immediate system halt and safe return to home position.
Safety Features: Fully enclosed electronics and controlled shutdown mechanisms to prevent hazards.

## Slide 4
System Architecture Overview
The pen plotter integrates diverse components for precise motion and control, ensuring robust operation.
1
Central Control
ESP32: Chosen for its Wi-Fi capabilities and dual-core processing, ideal for real-time motor control and feedback processing.
2
Motor Control
DRV8833 & DC Motors: Dual DRV8833 drivers control two independent DC motors, enabling precise Core-XY motion.
3
Feedback & Safety
Optical Encoders & Limit Switches: Provide critical position feedback and boundary detection for safe and accurate operation.
4
Pen Actuation
Servo Motor: Controls the Z-axis (pen up/down) with high accuracy, ensuring clean lines and preventing surface damage.

## Slide 5
Mechanical Design & Fabrication
Every structural component of the pen plotter was custom-designed and 3D printed, emphasizing precision and modularity.
Software: Designed entirely in SolidWorks and Fusion 360, ensuring high precision and robust modeling.
Fabrication: All parts 3D printed with tight tolerances, guaranteeing accurate assembly and reliable performance.
Custom Components: Designed specific mounts for DC motors and encoders, a central carriage, pen holder with rack & pinion, and tensioners.
Emergency Stop Holder: Integrated for safety and accessibility, ensuring quick system shutdown.

## Slide 6
Core-XY Kinematics
The Core-XY configuration provides efficient and precise motion, minimizing moving mass and maximizing speed.
Two Stationary Motors
Positioned at fixed points, reducing inertia and improving response time.
Crossed GT2 Belts
Interconnected system ensures synchronized movement for the X and Y axes.
Motion Decoupling
X-axis: Motors rotate in opposite directions.
Y-axis: Motors rotate in the same direction.
Benefits
Offers high speed, simplicity in design, and precision in plotting.

## Slide 7
DC Motors & Synchronization Challenges
Achieving synchronized motion with standard DC motors proved more complex than anticipated.
Dual DC Motors: Used for Core-XY configuration, driving the X and Y axes.
RPM Mismatch: Even with identical PWM signals, motors exhibited varying rotational speeds, leading to cumulative errors.
Distortion Impact: Inconsistent motor speeds directly translated into distorted plotted lines, compromising drawing accuracy.
Solution Requirement: Highlighted the critical need for a fine-tuned control system to ensure perfect synchronization between the motors.

## Slide 8
PID Tuning & PWM Optimization
Implementing closed-loop PID control and fine-tuning PWM parameters were crucial for mitigating RPM discrepancies and enhancing plotting accuracy.
PID Implementation
Currently integrating a Proportional-Integral-Derivative (PID) controller for real-time closed-loop correction of motor RPMs.
PWM Resolution Adjustment
Increased PWM resolution to allow for finer control over motor speeds, minimizing small velocity deviations.
PWM Frequency Optimization
Optimized PWM frequency to ensure smoother motor operation and reduce vibrations, contributing to better plotting quality.
Drawing Sequence Logic
Revised the software logic for drawing sequences, allowing for dynamic adjustments and tighter synchronization between motor commands.
Software Calibration
Developed a software calibration routine that significantly reduced the inherent RPM offset between the two DC motors.

## Slide 9
Feedback System: Optical Encoders
Optical encoders provide essential real-time feedback, forming the backbone of our closed-loop control system.
Encoder Design: Each motor is equipped with a 20-slot wheel and an optocoupler, generating pulses for rotation detection.
Purpose: Provides critical RPM and angular position feedback to the ESP32, enabling precise motor synchronization and path tracking.
Closed-Loop Control: Essential for achieving the required accuracy in X and Y axis movements, correcting for motor inconsistencies.
Future Enhancement: Quadrature Encoders: Planned upgrade to improve resolution and provide directional information for enhanced precision.
Future Enhancement: Hall Effect Sensor: To be integrated for reliable paper presence detection, preventing plotting errors on empty surfaces.

## Slide 10
Z-Axis: Precise Pen Control
The Z-axis mechanism ensures consistent pen contact and clean, repeatable lines.
Servo Motor Actuation
A dedicated servo motor provides fine angular control for precise pen up/down movements.
Rack & Pinion Mechanism
Integrated directly into the pen holder, translating rotational servo motion into linear vertical movement of the pen.
Optimal Pen Contact
Ensures consistent pressure on the drawing surface, preventing skips while avoiding damage.
Repeatability
The mechanical design guarantees highly repeatable pen lifts and drops, critical for multi-pass drawings.

## Slide 11
Precision Plotting: Overcoming GT2 Belt Challenges
This presentation details the mechanical and software innovations in our custom CNC plotter, focusing on precision, safety, and future upgrades.

## Slide 12
Custom Tensioner Design
Initial runs revealed GT2 belt loosening, causing plot inaccuracies. We designed adjustable 3D-printed tensioners, allowing precise manual tightening to eliminate slack and ensure consistent belt tension. This significantly improved stability and accuracy.

## Slide 13
Limit Switches & Homing Logic
Dual Limit Switch Installation
Two mechanical limit switches were integrated: one at the left-front mount and another at the belt tensioner base. These provide precise physical boundaries for the plotter's movement.
Firmware Homing Function
A homing function was implemented in the ESP32 firmware. Upon power-up or command, the plotter automatically moves to a defined reference position, ensuring a consistent and accurate starting point for all operations.

## Slide 14
Emergency Stop & Resume
Immediate Motion Halt
The emergency stop feature instantly halts all plotter motion, preventing damage or injury in critical situations.
Position Saved to EEPROM
The plotter's current position is automatically saved to non-volatile EEPROM memory upon activation of the emergency stop.
Homing & Resume
After a reset, the machine first returns to its homing position, then recovers and resumes plotting from the exact point of interruption, ensuring seamless operation.

## Slide 15
Path Planning Logic
The plotter's path planning was custom-coded to accurately reproduce complex designs without relying on G-code in the initial phase.
Nikola’s House Segmented
The drawing of Nikola’s House was meticulously broken down into individual line segments for precise control.
Sequential Path Encoding
Each line segment's coordinates and drawing instructions were explicitly coded in sequence, dictating the plotter's movement.
Triple Loop Execution
The entire path was executed in a loop function, repeating three times to verify consistency and achieve the desired final output.
Axis Synchronization Focus
Critical attention was paid to ensuring perfect synchronization between all axes, vital for accurate and repeatable drawings.

## Slide 16
Testing & Debugging
During development, several key issues were identified and systematically addressed:
Loop closure inconsistencies
Suboptimal belt alignment
Motor synchronization drift
Encoder wiring noise interference
Intermittent circuit disconnects
A comprehensive suite of tools was utilized to diagnose and resolve these challenges:
Multimeter for circuit diagnostics
Serial monitor for real-time data inspection
Encoder monitoring for position feedback
Solutions involved stepwise testing, CAD model correction, and meticulous firmware tuning.

## Slide 17
Final Output – Nikola’s House
After extensive testing and fine-tuning, the plotter successfully rendered Nikola’s House three consecutive times without any noticeable drift or deviation. This achievement confirms the precision enhancements gained through mechanical adjustments and firmware optimization.

## Slide 18
Future Scope & Upgrades
Precision Feedback
Implement 2-channel quadrature encoders for enhanced positional accuracy and real-time feedback control.
G-code Compatibility
Integrate G-code parsing functionality, enabling compatibility with Inkscape and other CAD/CAM software for diverse design inputs.
Dedicated Controller
Utilize a secondary ESP32 as a dedicated parsing controller, offloading processing from the main MCU and improving efficiency.
Wireless Interface
Develop an optional Wi-Fi or Bluetooth user interface for remote commands and real-time monitoring of plotter operations.
Motor Upgrade
Transition to high-precision stepper motors for ultra-high resolution and smoother motion, catering to advanced plotting needs.

## Slide 19
Conclusion & Learnings
Developed Strong Skills In:
Mechatronics integration
Embedded coding (ESP32)
CAD & 3D printing
Real-time debugging
Learned Importance Of:
Robust feedback control systems
Modular mechanical design principles
System safety & recovery handling

## Slide 20
Thank You / Q&A
Thank you for your attention and interest in our CNC plotter project. We are now open for any questions or feedback you may have.